991.1 Car Info from PCNA

“Nothing defines us more than our heritage. It says a lot about who we are. This is particularly true of the 911 Carrera S, which has all the characteristics you would expect of a sports car whose origin is in motorsport. An elementary component of its DNA, therefore, is power in the form of a 3.8-litre engine with direct fuel injection (DFI) and VarioCam Plus. It delivers 294 kW (400 hp) at 7,400 rpm, and the maximum torque of 440 Nm is achieved at 5,600 rpm. In conjunction with the manual gearbox, the sprint from 0 to 100 km/h is completed in just 4.5 seconds. Top speed isn’t reached until 304 km/h. On figures alone, the 911 Carrera S excels, particularly in terms of efficiency. Fuel consumption and CO2 emissions have been reduced by 15% compared with the previous model. This has been possible thanks to the auto start/stop function, which is available as standard, and the coasting function in conjunction with the optional Porsche Doppelkupplung (PDK). It’s not difficult to tell where the 911 Carrera S comes from. You can hear it in the resonant engine sound and you can see it in the twin tailpipes in brushed stainless steel and 20-inch Carrera S wheels.

You can also feel it, thanks to Porsche Active Suspension Management (PASM), which is fitted as standard, or the optional PASM sports suspension with even sportier aerodynamics and the ride height lowered by 20 mm. Or the optional Sport Chrono Package and dynamic engine mounts.

Available as standard, Porsche Torque Vectoring (PTV), or Porsche Torque Vectoring Plus (PTV Plus) in conjunction with the optional PDK, increase traction and driving stability. Porsche Dynamic Chassis Control (PDCC), the active roll stabilisation system, is available as an option and improves agility, comfort and safety. On the subject of safety, the brakes at the front of the 911 Carrera S come equipped with monobloc fixed calipers with six, instead of four, pistons for improved braking performance and a shorter braking distance. Bi-Xenon headlights are standard and the Porsche Dynamic Light System (PDLS) is available as an option. There is no doubt. The 911 Carrera S knows its roots, and embraces them with efficiency, power and sporty performance.”

More from PCNA, 2013 911 Brochure

“The new 911 Carrera was created to redefine the everyday driving experience, delivering exhilarating performance with surprising practicality. Although its engine displacement has been reduced to 3.4 liters, it generates more power and faster acceleration than its celebrated 3.6-liter predecessor, sprinting from 0–60 mph
in just 4.6 seconds—4.2 seconds when equipped with the optional Porsche Doppelkupplung (PDK) transmission and the Sport Chrono Package.

Advanced Powertrain

How did Porsche engineers balance the sensible with the sensational? The new thermal management technology manipulates heat flow to bring engine and transmission to optimal operation temperatures faster, reducing fuel consumption. Electrical system recuperation reduces the alternator’s draw on engine power, freeing it for pure exhilaration.

Other benefits come from a choice of two advanced transmissions, including a seven-speed manual gearbox. The first six forward gears have a sport ratio, while the seventh has a long ratio that reduces fuel consumption and engine noise at highway cruising speeds. The optional PDK also employs seven forward gears with a long- ratio top gear for efficient cruising. A new addition to PDK is the ingenious coasting function, which eliminates engine braking in certain conditions for even greater fuel efficiency.

The Sport button, which is fitted as standard in the 911 Carrera, makes
it possible to select an even more responsive engine performance program. In vehicles equipped with PDK, the Sport button also selects more aggressive shift points when in automatic mode.

Sportiness and Safety

The new 911 Carrera is fitted as standard with 19-inch wheels,
which improve driving stability and performance while enhancing the car’s visual presence. Powerful braking is provided by four-piston, aluminum monobloc brakes with black calipers, and optimized with ABS (Anti-lock Brake System) and standard Porsche Stability Management (PSM). In addition to helping provide stabilty, PSM improves braking response and braking power in emergency conditions.

With its potent and efficient powertrain, luxurious and purposeful interior,
and outstanding performance and safety, the 911 Carrera delivers a rare combination of driving passion and everyday practicality.

The New 911 | The 911 Carrera

Passion meets practicality. The new 911 Carrera.

One letter can say quite a lot. For Porsche, “S” designates the superlative form of the 911 Carrera. In the new Carrera S, track-ready performance is taken to a new level through a host of engine and chassis advancements. Impressively, its improved power and agility coexist with fuel efficiency.

400 Horsepower with Efficiency

The new Carrera S achieves 400 horsepower from a 3.8-liter boxer engine. The engine benefits greatly from Porsche’s ongoing development of VarioCam Plus, which optimizes power and torque at all engine speeds, and Direct Fuel Injection (DFI), which improves combustion.

A suite of innovations—including the standard Auto Start Stop function, thermal management, and electrical system recuperation—provides even greater fuel efficiency while freeing more power.

Commanding Acceleration

The new Carrera S accelerates from 0–60 mph in a breathtaking 4.3 seconds, and achieves a top track speed of 188 mph. When equipped with the optional PDK and Sport Chrono Package, it sprints from 0–60 in just 3.9 seconds.

Other Carrera S Sensations

Outstanding acceleration is just one sensation that sets the Carrera S apart. Visually, its standard 20-inch wheels make a bold statement while also improving stability. The resonant engine sound is enhanced by two matched pairs of brushed stainless steel tailpipes.

One also feels the superlative damping control of Porsche Active Suspension Management (PASM) and the increased agility and steering precision of Porsche Torque Vectoring (PTV), both standard in the Carrera S.

Shorter Braking Distance

For the first time, the new 911 Carrera S features front brakes with six (rather than four) pistons in a solid monobloc red caliper, resulting in even shorter braking distance.

The 911 Carrera S has always been a bold expression of the 911 Carrera character. In the new Carrera S, the performance envelope has expanded to embrace greater efficiency for a new century.

The verbiage below is off the Naples FL Porsche dealer web site. Certified. 2013 Porsche 911 Carrera S Agate Gray Metallic 7-Speed Porsche Doppelkupplung (PDK) 3.8L H6 DI 400 hp Clean Carfax, One Owner, Local Trade, 20  Sport Design Wheels, ABS brakes, DVD-Audio, Electronic Stability Control, Front dual zone A/C, Heated door mirrors, Illuminated entry, Low tire pressure warning, Navigation System, Rear Lights in Clear Glass Optics, Remote keyless entry, Traction control.

Porsche Approved Certified Pre-Owned Details:

MECHANICAL

    - Vario-cam plus variable valve timing system

    - Porsche torque vectoring (PTV) -inc: limited slip rear differential lock

    - Rear wheel drive

    - Full underbody paneling

    - McPherson front suspension

    - LSA multi-link rear suspension

    - Front/rear stabilizer bars

    - Porsche active suspension management system (PASM) -inc: electronic damper control system w/two manually selectable settings

    - Pwr assisted rack & pinion steering w/variable ratio

    - Pwr 4-wheel vented disc brakes -inc: 6-piston front/4-piston rear monobloc fixed alloy calipers

    - Front/rear brake pad-wear sensors

    - Brake calipers painted in red

    - Electric parking brake

    - Four-pass multi-flow exhaust system w/(2) dual-tube tailpipes in brushed stainless steel , valve control

EXTERIOR

    - 20" x 8.5" front/20" x 11" rear Carrera S aluminum wheels -inc: P245/35ZR20 front tires, P305/30ZR20 rear tires

    - Tire sealing compound w/electric air compressor

    - Roof transport system preparation

    - Front apron w/integrated air intakes

    - Automatic extending rear spoiler

    - Rear lid model designation & "PORSCHE" in chrome

    - Auto on/off headlights

    - Bi-xenon headlights -inc: auto leveling, washers, welcome home function

    - LED turn signals

    - Rear fog light

    - LED tail lights & brake lights

    - Pwr folding heated mirrors w/memory

    - Rain-sensing intermittent windshield wipers w/heated washers

    - Doors & trunk lid in aluminum

    - Windscreen w/grey top tint

ENTERTAINMENT

    - CD3-31 AM/FM stereo w/CD player -inc: 7" color touchscreen

    - Sound pkg plus -inc: analogue sound-system w/CD storage in glove compartment, (9) speakers w/235 watt output

    - PCM navigation module -inc: 40GB HDD, dynamic route calculation, extended navigation, electronic logbook, voice control

    - Universal audio interface -inc: connections for iPod, USB for memory stick w/MP3 files, aux input

    - Bluetooth interface for mobile phone preparation

INTERIOR

    - Sport pwr bucket seats -inc: driver & front passenger seat pwr backrest, driver & front passenger seat pwr height, driver & front passenger seat manual fore/aft

    - Partial leather seat trim

    - Leather front seat side bolsters & headrests

    - Front seat extended integrated headrests

    - Split-folding rear bench seat

    - Storage behind rear seats

    - (3) door brake rest positions

    - (4) floor mats

    - Front/rear door storage compartments

    - (3) storage compartments in center console

    - Tilt/telescopic steering wheel

    - Steering wheel in leather w/audio/on-board computer controls

    - Pwr front windows w/one-touch

    - Remote central locking w/pwr hood & trunk release

    - Keyless entry

    - HomeLink garage door opener

    - Cruise control

    - On-board computer

    - Immobilizer system w/in-key transponder, alarm system & radar-based interior surveillance

    - Integrated cluster of (5) round instruments

    - Instrument dials painted in silver

    - Gear lever & handbrake trim in leather

    - Automatic climate control -inc: active carbon filter

    - Heated rear screen

    - Door entry guards w/model logo

    - Roofliner in black Alcantara

    - Illuminated visor vanity mirrors

    - Coat hooks on front seatbacks

    - Dual front cup holders

    - Large lockable glovebox

    - Lighting -inc: reading lights, orientation lights, ignition lock, vanity mirror lighting, front footwell, glove compartment, luggage compartment, exit lighting, white interior lighting w/dimming

    - (3) 12v pwr outlet

SAFETY

    - Daytime running lights

    - Front/rear deformable aprons w/integrated alloy bumpers mounted on impact absorbers

    - Driver & front passenger airbags -inc: front passenger on/off switch

    - Porsche side impact protection system (POSIP) -inc: driver & front passenger side airbags, driver & front passenger integrated thorax airbags in seat backrests & head airbag in each door panel.