CAR NUMBER

SAFETY INSPECTION CHECKLIST	RUN GROUP _______________

This form has been updated! Please read all of it and make sure it is completely filled out!

TRACK EVENT PARTICIPANTS ARE PRIMARILY RESPONSIBLE FOR THE SAFETY OF THEIR CAR AND SHOULD KNOW THE CONDITION OF ALL ITEMS ON THIS LIST.  DURING SAFETY INSPECTIONS, THE OWNER OR OPERATOR MUST REMAIN WITH HIS OR HER CAR AND OPERATE IT AS REQUESTED BY THE SAFETY INSPECTOR.

DRIVER MUST COMPLETE THE FOLLOWING:

EVENT NAME AND DATE(S)

P	F	DRIVER(S) NAME(S)

A	A

S	I	ADDRESS	CITY	STATE	ZIP

S	L

E	E	CAR TYPE	YEAR	LICENSE PLATE

D	D

THE FOLLOWING WILL BE CHECKED ON THE GROUND:

[   ]	[   ]	1.	BRAKE LIGHTS: Must be functional.

[   ]	[   ]	2.	WINDSHIELD: No cracks in windshield or in any other windows. Wipers must be functional and wiper blades in good condition.

[   ]	[   ]	3.	MIRRORS: Rear-view mirrors must be securely mounted; must have at least one rear-view mirror.

[   ]	[   ]	4.	FIRE EXTINGUISHER: Must be securely mounted (metal to metal) within reach of driver.  Must be BC or ABC rated, 2.5 lb minimum and must be fully charged.  HALON type is highly recommended. Required in White run group and above; highly recommended for all others.

[   ]	[   ]	5.	HELMET(S): Must carry a 2005 or 2000 Snell M or SA sticker; SA highly recommended.

[   ]	[   ]	6 .	PEDALS: All pedals must have free return and be in good operating condition. Brake pedal must be FIRM.

[   ]	[   ]	7.	SEAT BELTS: Metal-to-metal seat belts securely mounted (driver and passenger). 1965-68 900 series must modify outer seat belt anchors so that the belt crosses the pelvic bone and lower abdomen and down toward anchor as near to 45 degrees as possible.  4- POINT HARNESSES ARE NOT PERMITTED. 5-POINT OR 6-POINT SAFETY HARNESS MAY NOT BE USED WITH STOCK HIGH-BACK PORSCHE SEATS. The installation of non-factory restraint systems must meet Manufacturers Safety Specifications. ON VEHICLES IN WHICH A PASSENGER MAY BE CARRIED (i.e., STUDENTS REQUIRING INSTRUCTORS OR INSTRUCTORS CARRYING STUDENTS), THE DRIVER AND PASSENGER SEATS AND RESTRAINT SYSTEMS MUST BE MATCHING OR SIMILAR.  ALL NON-FACTORY BELTS MUST HAVE A CLEAR DATE AND BE LESS THAN 5 YEARS OLD.

[   ]	[   ]	8.	ROLL BARS: All open cars (except Targas and 914s), soft tops and open race cars, must have adequate roll bars. The deployable roll bar in a 996-997 cabriolet is adequate for all tracks except VIR and Lime Rock.  The driver in all open cars, including Boxsters, will be subject to the broomstick test. Pre-2005 Boxsters require Brey-Krause bar for VIR.  Roll bars must be covered with closed cell foam padding in any place where a helmet could come in contact with the bar.

[   ]	[   ]	9.	BRAKE FLUID: Sufficient brake fluid, DOT 3 or 4 recommended.  Brakes should be bled prior to all high-speed track events.  Brake fluid must be changed at least annually.  Date on which brake fluid was last changed ______________________.

[   ]	[   ]	10. 	BATTERY(IES): Securely fastened and in good condition.  No acid leaks or corrosion.  Check fuel lines under battery tray on 914.

[   ]	[   ]	11.	FAN BELTS: Fan and other belts tight and in good condition.

[   ]	[   ]	12.	THROTTLE RETURN: Freely operating linkage and good springs: both return springs on CIS cars.

[   ]	[   ]	13.	AUXILIARY EQUIPMENT: The mounting and installation of all permanently installed auxiliary equipment must be inspected for safety. This includes car phones, radar detectors, sound equipment, and data-acquisition devices. The use of in-car video equipment is restricted to those run groups not requiring instructors.  The complete camera must be installed at this inspection and secured metal to metal, including a safety strap around the camera and the roll bar such as A METAL BAND CLAMP, not a cloth strap.  The Tech Inspector will check each applicable item below and indicate PASS or FAIL.

RADAR DETECTOR	______________           PHONE                                   ______________

SOUND/VIDEO EQUIP.	______________           DATA ACQUISITION/OTHER	______________

THE FOLLOWING ITEMS WILL BE CHECKED ON THE LIFT:

[   ]	[   ]	14.	FRONT SUSPENSION: No excessive looseness in steering or suspension. Lower trailing arm to radius arm tight; axle and shock bolts tight; no fluid leaks; ball joints in good condition; tie rods secure; axle boots and oil seals in good condition. 900 series - tight mounting of steering rack. 944, inspect lower control arm for loose ball joints and cracks. NOTE: all LOWERED 944’s are prone to catastrophic failure of the ball joint.

[   ]	[   ]	15.	WHEEL BEARINGS: Correct adjustment (check rear bearings where applicable).

[   ]	[   ]	16.	BRAKES: Sufficient brake linings or pads, 50% min.  914 check inner rear pads.  No cuts or abrasions in brake lines.  Check rotor condition. There should be no visible cracks extending to the edge of the rotor.

[   ]	[   ]	17.	WHEELS: No cracks or bends.  All lug nuts engaged.  Valve stems must have airtight caps.  Pay special attention to after market wheels and Turbo Twist wheels.  If using track tires, steel lug nuts should be used.

[   ]	[   ]	18. 	TIRES: No cracks and in good condition.  Minimum 3/32" tread depth on contact patch area (except race tires).  Extra wide tires, wheels and fender flares subject to Inspector's approval.  All tires should be of the same manufacturer and type.  Front tires should be the same size.  Rear tires should be the same size.

[   ]	[   ]	19.	LEAKS: No leaks of any fluids (oil, gas, brake fluid or coolant).

[   ]	[   ]	20.	EXHAUST SYSTEM: Securely fastened and in acceptable condition.

[   ]	[   ]	21.	REAR SUSPENSION: Check half shaft bolts and shock bolts.  Check fuel pump, fuel lines on 914.

[   ]	[   ]	22.	RUST.  No excessive rust or damage to suspension / chassis parts.

INSPECTOR(S) ARE NOT LIABLE FOR THE SAFETY OF THIS VEHICLE

INSPECTED BY:	DATE:

OWNER HAS FINAL RESPONSIBILITY FOR THE SAFETY OF THIS VEHICLE

OWNER SIGNATURE:	DATE:

# Text boxes

2009 Pre-Tech Form

Bring this completed form to the track. It will be part of the morning tech session.

Will the tires on the vehicle at the time of this inspection be the tires used at the track?  yes/no (circle)