Trunk lid switch

I took the door sill off and took the switch apart. It showed some corrosion on the contacts. It's a bad design because if you get any water from the rain on the switch, the water goes right in and over the switch.
One of the wires on the circuit board had a bad connection so i just re-solder it.
I put a bit of dialectric grease around it, works like a champ.

Remove the small plugs facing the driver seat and use a 5mm allen wrench and just loosen the bolts (through the holes that were covered by the plugs) that keep the sill in place , don't need to take them out! Then just pull the sill up. 
http://www.planet-9.com/cayman-boxster-chat/48176-doorsill-removal.html

- Pry off the caps to the sill—they face the driver's seat. This is part #8 in the diagram.

(2) Use an Allen wrench (I do not recall the size) to remove the two bolts. This is part #7 in the diagram.

(3) I then used one of the nylon tools from my "Trim & Molding Tool Kit" to pry up the sill. It will make some noise in the process because of the expander nut (part #6 in the diagram).

(4) Unplug the electrical connection and remove the sill.

(5) Installation is the reverse of removal.

- I had to insert the long end of the allen wrench in the hole exposed by the removal of the caps. One of the holes was a bit harder to access with the allen wrench than the other.

- One thing I do remember to make the process a bit easier: its not neccessary to completely remove the bolts - just loosen the bolts and the sill can be removed. That way when you reinstall the sill you avoid the hassle of trying to find the respective hole for the bolts to be reinserted.

Size is smaller than 6 mm and at quite an angle from the hole in the doorsill. Didn't read your post about not removing them all the way so had more fun lining them up to reinstall. But the new switch operates the front trunk so all is well.